## Slide 1: Simulation Study of Droplet formation in T Junction
Mitanshu Kansal (2020CH70180)
Lalwala Taukir Mohamad (2020CH70174)
CLL770 – Term Project

## Slide 2
Introduction
Microfluidics is a cutting-edge field which manipulates fluids at the microscale to achieve precise control over physical and chemical process.
The field play a vital role in applications such as:
Drug delivery systems
Diagnostic tools for medical research
Droplet formation is a core mechanism in microfluidic systems enabling generation of uniform droplets for chemical reactions.
It involves interaction of two immiscible fluids usually in at a junction
[1]: Filimonov, R., Wu, Z., & Sundén, B. (2021). Toward computationally effective modeling and simulation of droplet formation in microchannel junctions. In Chemical Engineering Research and Design (Vol. 166, pp. 135–147). Elsevier BV. https://doi.org/10.1016/j.cherd.2020.11.010
Fig: Lab on a chip[1]
Fig: Droplet formation[1]

## Slide 3
Research Paper overview
Simulate droplet formation in T-Junction microfluidic channels
Study conducted on key parameters:
  Flowrate Ratio
  Viscosity
  Interfacial Tension
  Contact Angle
Simulation validated against experimental data
Fig.: Droplet Formation from Simulation[1]
Fig.: Droplet Formation from Experiment[1]
[1]: Filimonov, R., Wu, Z., & Sundén, B. (2021). Toward computationally effective modeling and simulation of droplet formation in microchannel junctions. In Chemical Engineering Research and Design (Vol. 166, pp. 135–147). Elsevier BV. https://doi.org/10.1016/j.cherd.2020.11.010

## Slide 4
Details on Simulation Done
Geometry Generated using the dimensions provided in research paper using Spaceclaim
Fig.: Schematic of Geometry[1]
[1]: Filimonov, R., Wu, Z., & Sundén, B. (2021). Toward computationally effective modeling and simulation of droplet formation in microchannel junctions. In Chemical Engineering Research and Design (Vol. 166, pp. 135–147). Elsevier BV. https://doi.org/10.1016/j.cherd.2020.11.010

## Slide 5
Details on Simulation Done
Generate Mesh with Element size of 0.1 mm.
Table: Statistics of the mesh generated

## Slide 6
Details on Simulation Done
Fluid used through the Microchannel:
Water liquid
  Density: 998.2 kg/m2
  Viscosity: 0.001003 kg/m-s
Oil
  Density: 1000 kg/m2
  Viscosity: 0.00671 kg/m-s
Contact Angle between the fluids: 135°
Velocity of Water = 0.01 m/s
Velocity of Oil = 0.01m/s

## Slide 7
Simulation of droplet formation

## Slide 8
Simulation of droplet formation

## Slide 9
Literature Results
Fig.: Droplet and Water Slug length vs. Contact Angle [1]
[1]: Filimonov, R., Wu, Z., & Sundén, B. (2021). Toward computationally effective modeling and simulation of droplet formation in microchannel junctions. In Chemical Engineering Research and Design (Vol. 166, pp. 135–147). Elsevier BV. https://doi.org/10.1016/j.cherd.2020.11.010

## Slide 10
Results and conclusion
0.4mm
0.8mm
0.64mm
Our Results:
Droplet Length = 0.64mm
Water Slug Length = 0.8 mm
From Literature [1]:
Droplet Length = 0.48mm
Water Slug Length = 0.49 mm
[1]: Filimonov, R., Wu, Z., & Sundén, B. (2021). Toward computationally effective modeling and simulation of droplet formation in microchannel junctions. In Chemical Engineering Research and Design (Vol. 166, pp. 135–147). Elsevier BV. https://doi.org/10.1016/j.cherd.2020.11.010